RS232 / USB-Converter fourfold

Pos.   )		pcs.

RS232 / USB-Converter fourfold to convert up to four RS232-Interfaceports (DB9) to one USB-Interface Port to the PC. Easy configuration via software. The USB / RS232-Converter allows the connection of up to 4 EGA-lines via EGA / PC-Interfaces-2, on the CGVision visualisation-,  monitoring- and programming software with only one USB-port.

Inclusive driver-CD and USB-cable.

Power supply:	5V, via USB-port

Power consumption: 	max. 500mA

RS232 ports:	4 x DB9 (COM)

Port to the PC:	1 x USB

Dimensions:	L=183mm, W=110mm, H=30mm

Weight: 	approx. 300g

Degree of protection: 	IP20

LED-display: 	multi colour status-LED

Type: RS232 / USB - Converter fourfold

Manufactured by: CEAG